## Slide 1: SSH Protocol

## Slide 2: Difference between Telnet and SSH
Telnet and SSH have the same purpose and both of them used to communicate to a remote device.
But telnet is not secure because all the data would be send in clear text including the passwords without authentication and encryption but where SSH is a secure protocol because it encrypt the data using authentication.

## Slide 3: Telnet
It works on port number 23
It is not secure protocol.
No data encryption

## Slide 4: SSH
Secure shell is a secure method for remote access as is include authentication and encryption. To do this it uses a RSA public/private key pair.
It works on Port Number 22.
Very secure protocol.

## Slide 5: SSH IN GNS3
Take new project in GNS3
Assign a name to the project (ssh)
Drag and drop two routers
Right click and change the symbol
Right click and select Auto-IDLE pc for both
Use ethernet to connect both the wires
Click start

## Slide 6: Console
Open R1 and R2 console
In R1 console type
config t
enable password admin
int f0/0

## Slide 7: Assign IP address
Type below commands for assigning
ip add 192.168.1.1 255.255.255.0
no sh
Ctrl + Z
Type below command to verify
sh ip int br

## Slide 8: Configure Router 2
Open Console and type below commands
ip add 192.168.1.2 255.255.255.0
no sh
Ctrl + Z
Type below command to verify
sh ip int br

## Slide 9: Open wireshark
by right click and start capture on ethernet

## Slide 10: At R2 console
Type
config t
ip ?

## Slide 11: RSA
crypto key generate rsa
800
Give version of ssh
ip ssh version 2
4. Assign users
line vty 0 5
5. transport input ?

## Slide 12: Set SSH
transport input ssh
login local
username admin password cisco
Ctrl+Z
Save by typing wr
sh run

## Slide 13: Now perform Remote login from Router 1
Type
ssh –l admin 192.168.1.2
2. Type
en
3. sh run

## Slide 14
THANK YOU